CSE3213 Computer Network I
CSE3213 Computer Network I
Medium Access Control Protocols
(Ch. 6.1 – 6.3)
Course page:
http://www.cse.yorku.ca/course/3213
Slides modified from Alberto Leon-Garcia and Indra Widjaja

---
Chapter Overview
Chapter Overview
Broadcast Networks
  - All information sent to all users
  - No routing
  - Shared media
  - Radio
    - Cellular telephony
    - Wireless LANs
  - Copper & Optical
    - Ethernet LANs
    - Cable Modem Access
Medium Access Control
  - To coordinate access to shared medium
  - Data link layer since direct transfer of frames
Local Area Networks
  - High-speed, low-cost communications between co-located computers
  - Typically based on broadcast networks
  - Simple & cheap
  - Limited number of users

---
Multiple Access Communications
Multiple Access Communications

---
Multiple Access Communications
Shared media basis for broadcast networks
  - Inexpensive: radio over air; copper or coaxial cable
  - M users communicate by broadcasting into medium
Key issue: How to share the medium?

1
2
3
4
5
M
Shared multiple
access medium

---
Approaches to Media Sharing
Approaches to Media Sharing
Medium sharing techniques
Static channelization
Dynamic medium access control
Partition medium
Dedicated allocation to users
Satellite transmission
Cellular Telephone
Scheduling
Random access
Polling: take turns
Request for slot in transmission schedule
Token ring
Wireless LANs
Loose coordination
Send, wait, retry if necessary
Aloha
Ethernet

---
Channelization:  Satellite
Channelization: Satellite
Satellite Channel
downlink fout
uplink fin

---
Channelization:  Cellular
Channelization: Cellular
uplink f1 ; downlink f2
uplink f3 ; downlink f4

---
Scheduling:  Polling
Scheduling: Polling
Data from 1
Data from 2
Poll 1
Data to M
Poll 2
M
2
1
3
Inbound line
Outbound line
Host
computer
Stations

---
Scheduling:  Token-Passing
Scheduling: Token-Passing
Ring networks
token
Data to M
token
Station that holds token transmits into ring

---
Random Access
Random Access
Multitapped Bus
Transmit when ready
Transmissions can occur; need retransmission strategy
Crash!!

---
Wireless LAN
Wireless LAN
AdHoc: station-to-station
Infrastructure: stations to base station
Random access & polling

---
Selecting a Medium Access Control
Selecting a Medium Access Control
Applications
  - What type of traffic?
  - Voice streams? Steady traffic, low delay/jitter
  - Data? Short messages? Web page downloads?
  - Enterprise or Consumer market? Reliability, cost
Scale
  - How much traffic can be carried?
  - How many users can be supported?
Current Examples:
  - Design MAC to provide wireless DSL-equivalent access to rural communities
  - Design MAC to provide Wireless-LAN-equivalent access to mobile users (user in car travelling at 130 km/hr)

---
Delay-Bandwidth Product
Delay-Bandwidth Product
Delay-bandwidth product key parameter
  - Coordination in sharing medium involves using bandwidth (explicitly or implicitly)
  - Difficulty of coordination commensurate with delay-bandwidth product
Simple two-station example
  - Station with frame to send listens to medium and transmits if medium found idle
  - Station monitors medium to detect collision
  - If collision occurs, station that begin transmitting earlier retransmits (propagation time is known)

---
Two-Station MAC Example
Two-Station MAC Example
Two stations are trying to share a common medium
Distance d meters
tprop = d /  seconds
A transmits at t = 0
A
B
A
B
B does not transmit before t = tprop & A captures channel
Case 1
B transmits before t = tprop and detects
collision soon
thereafter
A
B
A
B
A detects
collision at
t = 2 tprop
Case 2

---
Efficiency of Two-Station Example
Efficiency of Two-Station Example
Each frame transmission requires 2tprop of quiet time
  - Station B needs to be quiet tprop before and after time when Station A transmits
  - R transmission bit rate
  - L bits/frame
size 12{ bold "Efficiency"=ρ rSub { size 8{"max"} } = { {L} over {L+2t rSub { size 8{ ital "prop"} } R} } = { {1} over {1+2t rSub { size 8{ ital "prop"} } R/L} } = { {1} over {1+2a} } } {}
size 12{ bold "MaxThroughput"=R rSub { size 8{ ital "eff"} } = { {L} over {L/R+2t rSub { size 8{ ital "prop"} } } } = { {1} over {1+2a} } R" ""bits/second"} {}
Normalized Delay-Bandwidth Product
size 12{a= { {t rSub { size 8{ ital "prop"} } } over {L/R} } } {}
Propagation delay
Time to transmit a frame

---
Typical MAC Efficiencies
Typical MAC Efficiencies
Two-Station Example:
size 12{ bold "Efficiency"= { {1} over {1+2a} } } {}
If a<<1, then efficiency close to 100%
As a approaches 1, the efficiency becomes low
CSMA-CD (Ethernet) protocol:
size 12{ bold "Efficiency"= { {1} over {1+6 "." "44"a} } } {}
Token-ring network
size 12{ bold "Efficiency"= { {1} over {1+ { {a}} sup { ' }} } } {}
a΄= latency of the ring (bits)/average frame length

---
Typical Delay-Bandwidth Products
Typical Delay-Bandwidth Products
Distance	10 Mbps	100 Mbps	1 Gbps	Network Type
1 m	3.33 x 10-02	3.33 x 10-01	3.33 x 100	Desk area network
100 m	3.33 x 1001	3.33 x 1002	3.33 x 1003	Local area network
10 km	3.33 x 1002	3.33 x 1003	3.33 x 1004	Metropolitan area network
1000 km	3.33 x 1004	3.33 x 1005	3.33 x 1006	Wide area network
100000 km	3.33 x 1006	3.33 x 1007	3.33 x 1008	Global area network
- Max size Ethernet frame: 1500 bytes = 12000 bits
- Long and/or fat pipes give large a

---
MAC protocol features
MAC protocol features
- Delay-bandwidth product
- Efficiency
- Transfer delay
- Fairness
- Reliability
- Capability to carry different types of traffic
- Quality of service
- Cost

---
MAC Delay Performance
MAC Delay Performance
Frame transfer delay
  - From first bit of frame arrives at source MAC
  - To last bit of frame delivered at destination MAC
Throughput
  - Actual transfer rate through the shared medium
  - Measured in frames/sec or bits/sec
Parameters
  R bits/sec & L bits/frame
  X=L/R seconds/frame
   frames/second average arrival rate
  Load  =  X, rate at which “work” arrives
  Maximum throughput (@100% efficiency): R/L fr/sec

---
Normalized Delay versus Load
Normalized Delay versus Load
E[T] = average frame
transfer delay
At low arrival rate, only frame transmission time
At high arrival rates, increasingly longer waits to access channel
Max efficiency typically less than 100%
X = average frame
transmission time
Load
Transfer delay
E[T]/X

max
1
1

---
Dependence on Rtprop/L
Dependence on Rtprop/L
Transfer Delay
Load
E[T]/X

max
1
1
max
a
a
a > a

---
Random Access

---
ALOHA
ALOHA
- Wireless link to provide data transfer between main campus & remote campuses of University of Hawaii
- Simplest solution: just do it
  - A station transmits whenever it has data to transmit
  - If more than one frames are transmitted, they interfere with each other (collide) and are lost
  - If ACK not received within timeout, then a station picks random backoff time (to avoid repeated collision)
  - Station retransmits frame after backoff time
First transmission
Retransmission
Backoff period B
t
t0
t0+X
t0-X
t0+X+2tprop + B
t0+X+2tprop
Vulnerable
period
Time-out

---
ALOHA Model
ALOHA Model
Definitions and assumptions
  - X frame transmission time (assume constant)
  - S: throughput (average # successful frame transmissions per X seconds)
  - G: load (average # transmission attempts per X sec.)
  - Psuccess : probability a frame transmission is successful
size 12{S= ital "GP" rSub { size 8{ ital "success"} } } {}
Any transmission that begins during vulnerable period leads to collision
Success if no arrivals during 2X seconds
X
X
frame transmission
Prior interval

---
Throughput of ALOHA
Throughput of ALOHA
size 12{S= ital "GP" rSub { size 8{ ital "success"} } = ital "Ge" rSup { size 8{ - 2G} } } {}
Collisions are means for coordinating access
Max throughput is max=1/2e (18.4%)
Bimodal behavior:
Small G, S≈G
Large G, S↓0
Collisions can snowball and drop throughput to zero
e-2 = 0.184

---
Slotted ALOHA
Slotted ALOHA
- Time is slotted in X seconds slots
- Stations synchronized to frame times
- Stations transmit frames in first slot after frame arrival
- Backoff intervals in multiples of slots
Backoff period B
t
(k+1)X
t0 +X+2tprop
kX
t0 +X+2tprop+ B
Time-out
Vulnerableperiod
Only frames that arrive during prior X seconds collide

---
Throughput of Slotted ALOHA
Throughput of Slotted ALOHA
alignl { stack { size 12{S= ital "GP" rSub { size 8{ ital "success"} } = ital "GP" \[ "no arrivals in X seconds" \] } {} # " "= ital "GP" \[ "no arrivals in n intervals" \] {} # " "=G \( 1 - p \) rSup { size 8{n} } =G \( 1 - { {G} over {n} } \) rSup { size 8{n} } rightarrow ital "Ge" rSup { size 8{ - G} } {} } } {}

---
Carrier Sensing Multiple Access (CSMA)
Carrier Sensing Multiple Access (CSMA)
A station senses the channel before it starts transmission
If busy, either wait or schedule backoff (different options)
If idle, start transmission
Vulnerable period is reduced to tprop (due to channel capture effect)
When collisions occur they involve entire frame transmission times
If tprop >X (or if a>1), no gain compared to ALOHA or slotted ALOHA
A
Station A begins transmission at t = 0
A
Station A captures
channel at t = tprop

---
CSMA Options
CSMA Options
Transmitter behavior when busy channel is sensed
  - 1-persistent CSMA (most greedy)
    - Start transmission as soon as the channel becomes idle
    - Low delay and low efficiency
  - Non-persistent CSMA (least greedy)
    - Wait a backoff period, then sense carrier again
    - High delay and high efficiency
  - p-persistent CSMA (adjustable greedy)
    - Wait till channel becomes idle, transmit with prob. p; or wait one mini-slot time & re-sense with probability 1-p
    - Delay and efficiency can be balanced
Sensing

---
1-Persistent CSMA Throughput
1-Persistent CSMA Throughput
Better than Aloha & slotted Aloha for small a
Worse than Aloha for a > 1

---
Non-Persistent CSMA Throughput
Non-Persistent CSMA Throughput
a = 0.01
S
Higher maximum throughput than 1-persistent for small a
Worse than Aloha for a > 1
0.81
0.51
a = 0.1
0.14
G
a = 1

---
CSMA with Collision Detection (CSMA/CD)
CSMA with Collision Detection (CSMA/CD)
Monitor for collisions & abort transmission
  - Stations with frames to send, first do carrier sensing
  - After beginning transmissions, stations continue listening to the medium to detect collisions
  - If collisions detected, all stations involved stop transmission, reschedule random backoff times, and try again at scheduled times
- In CSMA collisions result in wastage of X seconds spent transmitting an entire frame
- CSMA-CD reduces wastage to time to detect collision and abort transmission

---
CSMA/CD reaction time
CSMA/CD reaction time
It takes 2 tprop to find out if channel has been captured
A begins to
transmit at
t = 0
A
B
B begins to
transmit at
t = tprop- ;
B detects
collision at
t = tprop
A
B
A
B
A detects
collision at
t= 2 tprop- 

---
CSMA-CD Model
CSMA-CD Model
Assumptions
  - Collisions can be detected and resolved in 2tprop
  - Time slotted in 2tprop slots during contention periods
  - Assume n busy stations, and each may transmit with probability p in each contention time slot
  - Once the contention period is over (a station successfully occupies the channel), it takes X seconds for a frame to be transmitted
  - It takes tprop before the next contention period starts.
Busy
Contention
Busy
(a)
Time
Idle
Contention
Busy

---
CSMA/CD Throughput
CSMA/CD Throughput
Time
At maximum throughput, systems alternates between contention periods and frame transmission times
where:
R bits/sec, L bits/frame, X=L/R seconds/frame
a = tprop/X
 meters/sec. speed of light in medium
d meters is diameter of system
2e+1 = 6.44
Busy
Contention
Busy
Contention
Busy
Contention
Busy

---
CSMA-CD Application:  Ethernet
CSMA-CD Application: Ethernet
First Ethernet LAN standard used CSMA-CD
  - 1-persistent Carrier Sensing
  - R = 10 Mbps
  - tprop = 51.2 microseconds
    - 512 bits = 64 byte slot
    - accommodates 2.5 km + 4 repeaters
  - Truncated Binary Exponential Backoff
    - After nth collision, select backoff from {0, 1,…, 2k – 1}, where k=min(n, 10)

---
Throughput for Random Access MACs
Throughput for Random Access MACs
- For small a: CSMA-CD has best throughput
- For larger a: Aloha & slotted Aloha better throughput
ALOHA
Slotted ALOHA
1-P CSMA
Non-P CSMA
CSMA/CD
a
max

---
Carrier Sensing and Priority Transmission
Carrier Sensing and Priority Transmission
- Certain applications require faster response than others, e.g. ACK messages
- Impose different interframe times
  - High priority traffic sense channel for time 
  - Low priority traffic sense channel for time 
  - High priority traffic, if present, seizes channel first
This priority mechanism is used in IEEE 802.11 wireless LAN

---
Scheduling
Scheduling

---
Scheduling for Medium Access Control
Scheduling for Medium Access Control
Schedule frame transmissions to avoid collision in shared medium
  - More efficient channel utilization
  - Less variability in delays
  - Can provide fairness to stations
  - Increased computational or procedural complexity
Two main approaches
  - Reservation
  - Polling

---
Reservations Systems
Reservations Systems
Centralized systems: A central controller accepts requests from stations and issues grants to transmit
  - Frequency Division Duplex (FDD): Separate frequency bands for uplink & downlink
  - Time-Division Duplex (TDD): Uplink & downlink time-share the same channel
Distributed systems: Stations implement a decentralized algorithm to determine transmission order
Central
Controller

---
Reservation Systems
Reservation Systems
Reservation
interval
Frame
transmissions
d
r
d
d
r
d
d
d
Time
Cycle n
Cycle (n + 1)
r
=
Transmissions organized into cycles
Cycle: reservation interval + frame transmissions
Reservation interval has a minislot for each station to request reservations for frame transmissions
1
2
3
M

---
Reservation System Options
Reservation System Options
Centralized or distributed system
  - Centralized systems: A central controller listens to reservation information, decides order of transmission, issues grants
  - Distributed systems: Each station determines its slot for transmission from the reservation information
Single or Multiple Frames
  - Single frame reservation: Only one frame transmission can be reserved within a reservation cycle
  - Multiple frame reservation: More than one frame transmission can be reserved within a frame
Channelized or Random Access Reservations
  - Channelized (typically TDMA) reservation: Reservation messages from different stations are multiplexed without any risk of collision
  - Random access reservation: Each station transmits its reservation message randomly until the message goes through

---
Example
Example
Initially stations 3 & 5 have reservations to transmit frames
Station 8 becomes active and makes reservation
Cycle now also includes frame transmissions from station 8
t
r
3
5
r
3
5
r
3
5
8
r
3
5
8
r
3
(a)
t
r
3
5
r
3
5
r
3
5
8
r
3
5
8
r
3
8
(b)

---
Example:  GPRS
Example: GPRS
General Packet Radio Service
  - Packet data service in GSM cellular radio
  - GPRS devices, e.g. cellphones or laptops, send packet data over radio and then to Internet
  - Slotted Aloha MAC used for reservations
  - Single & multi-slot reservations supported

---
Reservation Systems and Quality of Service
Reservation Systems and Quality of Service
Different applications; different requirements
  - Immediate transfer for ACK frames
  - Low-delay transfer & steady bandwidth for voice
  - High-bandwidth for Web transfers
Reservation provide direct means for QoS
  - Stations makes requests per frame
  - Stations can request for persistent transmission access
  - Centralized controller issues grants
    - Preferred approach
  - Decentralized protocol allows stations to determine grants
    - Protocol must deal with error conditions when requests or grants are lost

---
Polling Systems
Polling Systems
- Centralized polling systems: A central controller transmits polling messages to stations according to a certain order
- Distributed polling systems: A permit for frame transmission is passed from station to station according to a certain order
- A signaling procedure exists for setting up order
Central
Controller

---
Polling System Options
Polling System Options
Service Limits: How much is a station allowed to transmit per poll?
  - Exhaustive: until station’s data buffer is empty (including new frame arrivals)
  - Gated: all data in buffer when poll arrives
  - Frame-Limited: one frame per poll
  - Time-Limited: up to some maximum time
Priority mechanisms
  - More bandwidth & lower delay for stations that appear multiple times in the polling list
  - Issue polls for stations with message of priority k or higher

---
Walk Time & Cycle Time
Walk Time & Cycle Time
- Assume polling order is round robin
- Time is “wasted” polling stations
  - Time to prepare & send polling message
  - Time for station to respond
- Walk time: from when a station completes transmission to when next station begins transmission
- Cycle time is between consecutive polls of a station
- Overhead/cycle = total walk time/cycle time
t
1
3
2
4
5
1
2
…
M
Frame transmissions
Polling messages
Cycle Time

---
Application:  Token-Passing Rings
Application: Token-Passing Rings
Free Token = Poll
Frame Delimiter is Token
Free = 01111110
Busy = 01111111
Listen mode
Delay
Input
from
ring
Output
to
ring
Ready station looks for free token
Flips bit to change free token to busy
Transmit mode
Delay
To device
From device
Ready station inserts its frames
Reinserts free token when done
token

---
Methods of Token Reinsertion
Methods of Token Reinsertion
- Ring latency: number of bits that can be simultaneously in transit on ring
- Multi-token operation
  - Free token transmitted immediately after last bit of data frame
Single-token operation
  - Free token inserted after last bit of the busy token is received back
  - Transmission time at least ring latency
  - If frame is longer than ring latency, equivalent to multi-token operation
Single-Frame operation
  - Free token inserted after transmitting station has received last bit of its frame
  - Equivalent to attaching trailer equal to ring latency
Busy token
Free token
Frame
Idle Fill

---
Application Examples
Application Examples
Single-frame reinsertion
  - IEEE 802.5 Token Ring LAN @ 4 Mbps
Single token reinsertion
  - IBM Token Ring @ 4 Mbps
Multitoken reinsertion
  - IEEE 802.5 and IBM Ring LANs @ 16 Mbps
  - FDDI Ring @ 50 Mbps
All of these LANs incorporate token priority mechanisms

---
Comparison of MAC approaches
Comparison of MAC approaches
Aloha & Slotted Aloha
  - Simple & quick transfer at very low load
  - Accommodates large number of low-traffic bursty users
  - Highly variable delay at moderate loads
  - Efficiency does not depend on a
CSMA-CD
  - Quick transfer and high efficiency for low delay-bandwidth product
  - Can accommodate large number of bursty users
  - Variable and unpredictable delay

---
Comparison of MAC approaches
Reservation
  - On-demand transmission of bursty or steady streams
  - Accommodates large number of low-traffic users with slotted Aloha reservations
  - Can incorporate QoS
  - Handles large delay-bandwidth product via delayed grants
Polling
  - Generalization of time-division multiplexing
  - Provides fairness through regular access opportunities
  - Can provide bounds on access delay
  - Performance deteriorates with large delay-bandwidth product